## Slide 1: Developing a Sustainable Transport System for Kosovo
Martin Humphreys
April 14, 2008
The European Union - The World Bank

## Slide 2: Three main messages
The current transport infrastructure is limited in scope and quality, and under increasing pressure;
The institutional framework and sector organizations, despite improvements, remain weak;
Development of Routes 6 and 7 are priorities for the authorities – but needs are far broader.

## Slide 3: Outline of the Presentation
The main challenges facing the transport sector.
The vision of the authorities.
What are the financing needs?

## Slide 4: A. The Main Challenges.

## Slide 5: The institutional framework
No coherent strategy of policy to guide development;
No updated inventory of all roads
Functional classification needs updating;
No consistent design and construction standards; Reform of the legal and policy framework for railways yet to start;
Air sector remains a reserved function.
New Law on Land Acquisition – remains to be tested;

## Slide 6: The organizations in the sector
Organization structure and responsibilities are in need of reform;
Inadequate allocations for maintenance at all levels of the road network;
No consistent use of asset management system;
Recent signs of strain in absorbing modest amounts of technical assistance and capacity building.

## Slide 7: The condition of the transport network
Network is isolated from wider regional network
Primary road network is (2005) in reasonable condition, but updated surveys are required;
One recent study found 94% of secondary and local roads are in poor or very poor condition;
and
Railway network has been neglected since end of conflict – and stock is old (although not life expired).

## Slide 8: Road safety is a major and growing economic and social issue

## Slide 9: Demand continues to grow
Reliable data on vehicle ownership is not available, but estimated rate 105 per 1000 head;
Vehicle use is predicated to grow at 3-6% pa; and
On Routes 6 and 7 levels range from 1900 AADT at N/S to over 27000 AADT around Pristina.

## Slide 10: On the railways

## Slide 11: B. What is the vision of the authorities?

## Slide 12: Vision for development of Sector
  Integration of the transport infrastructure of Kosovo into the international regional transport networks – priority construction of routes 6 and 7;
  Implementation of European standards in all transport sectors;
  Clear backlog and modernization existing infrastructure;
  Reducing the cost of transport to facilitate economic development; and
  Reducing the number of accidents in traffic;

## Slide 13
C. What are the financing needs?

## Slide 14: Maintaining the road network
Normal maintenance needs on primary/regional network - € 20 million (2006 € 8.1 mill);
Backlog additional €12 per year
Local Roads normal €12 mill per year;
Backlog additional €11 million per year; and
Total Maintenance needs €53.9 mill pa, or approx. €270 million over the next five years

## Slide 15: Developing the road network

## Slide 16: Phased implementation needs
Section | Recommended Intervention | Investment (€ million) | Remarks
Pristina – border with Serbia (Route 7) | Motorway close to Pristina, new 2 lane road between Podujeve and Besi and upgrade of existing road to the border with Serbia | 132.8 | Motorway project should be closely co-coordinated with the Pristina Ring Road project
Pristina – Border with Albania (Route 7) | Motorway between Pristina and Shtime and upgrade of existing road for other parts of the route | 133.4 | Motorway design should be optimized including a supplementary interchange at Lipjan
Pristina – Border with FYROM (Route 6) | New high standard 2-lane road between Pristina and Doganaj, and upgrade existing road to border | 97.5 | -
Pristina – Border with Montenegro (Route 6) | New high standard 2-lane road from bypass at Fushe Kosove to Komorane. Restoring design standards and smaller upgrading works on other parts of the route | 53.2 | Sections close to Pristina should be co-coordinated with the construction of the Fushe-kosove bypass
Total |  | 416.9 | 

## Slide 17: In the railway sector
  Following projects are considered to be priority projects in the short term:
    Technical assistance to strengthen the institutional framework, develop the new law on railways and other legislation and establish the railway regulatory body - € 1.5 million;
    Repair of existing freight wagons - € 2.5 million;
    Repair of existing locomotives - € 3.3 million; and
    Purchase of new diesel locomotives to replace life expired locomotives in the current fleet - € 10 million.

## Slide 18: Total Needs over the next 5 years
Conservative estimate is €1100 million over next 5 years - € 220 per year;
Average spend 2000-2006 €40 per annum (€90 mill in 2008);
Authorities predict €100 million from budget;
Estimated gap - €600 million in total.

## Slide 19
Thank you