## Slide 1
Mitigating Coal/Lignite Environmental Impacts: Kosovo C Case Study
Charles Feinstein, World Bank

## Slide 2: A view of Kosovo’s energy sector
Kosovo is rich with low-cost lignite resources with proven reserves estimated at around 12 billion tonnes.
Currently it has two power plants Kosovo A and Kosovo B built in 1960s and 1980s, respectively.
From total 1513 MW installed generating capacity, Kosovo has only around 600 MW available capacity due to age, poor prior maintenance, and damage caused during the war.
There is great amount of unmet demand for electricity both in Kosovo and SEE region-wide.

## Slide 3: Why do we need Kosovo C?
Energy and mining sectors in Kosovo are regarded as future pillars of economic growth and poverty reduction.
Consequently, Kosovo Provisional Institutions of Self-Government (PISG) has expressed interest in building new power plant that will increase electricity generation and lignite production.
PISG has invited several donors like European Commission, World Bank, USAID and KfW to support its development agenda by facilitating private investments in energy and mining sector.

## Slide 4: What are key facts?
Kosovo C power plant is expected to have an initial generating capacity of around 1000 MW. The on-going SESA study will give more clarification in this regard.
The overnight capital cost of Kosovo C power plant is estimated at €1.2 billion and it will be the first foreign direct investment of this scope in the region.
It requires 5 to 6 years for development and construction, with first unit(s) of Kosovo C power plant expected to come on-line around 2014.
Kosovo C represents an opportunity to adopt climate-friendly technology ahead of business-as-usual practice in the region.
Notes: total capital cost is determined by the size of the power plant and this number is taken from PAD according to which it responds to the 600MW power plant)

## Slide 5: How is World Bank involved in Kosovo C project?
Through IDA grant of $10.5 million, World Bank is offering technical assistance to Kosovo C project, formally known as Lignite Power Technical Assistance Project (LPTAP).
World Bank support in Kosovo C is organized around three main components: support to transaction, legal, and environment/social assessment advisors.
Additionally, World Bank is working hard to ensure that the bidding process will be open, transparent, and competitive.

## Slide 6: Proven technologies for lignite-fired power station
 | PF sub-critical units |  | PF 500MW supercritical units | CFB 300MW sub-critical units
 | 300 MW | 500MW |  | 
Capital cost | US$ 1,500 -2,000/kW | US$ 1,176 -1,764/kW | US$ 1,200 -1,800/kW | US$ 1,700 -2,200/kW
Lignite heat value (kJ/kg) (LHV) | 8200 | 8200 | 8200 | 8200
Net efficiency (LHV) | 38 - 40% | 38.2 – 40.2% | 40 - 42% | 38 - 40%
Heat rate (kJ/kWh) | 9474 - 9000 | 9427 - 8955 | 9000 - 8571 | 9474 - 9000
CO2 emission factor (tonnes/MWh) | 0.93-0.89 | 0.93-0.88 | 0.89-0.84 | 0.93-0.89

## Slide 7: Local/Regional Environmental Impact
Emissions Level for Kosovo A, Kosovo B, and forthcoming Kosovo C (in mg/Nm3):
 | SO2 | NOx | Dust
Kosovo A | 604 | 350 | 2000
Kosovo B | 693 | 756 | 260
Kosovo C | 200 | 200 | 50

## Slide 8: Global Environmental Impact
Level of CO2 emissions generated from Kosovo A, Kosovo B, and Kosovo C:
(@ 610 MW)
(@ 678 MW)
(@ 1000 MW)
Notes: CO2 emission factor for Kosovo A and Kosovo B are 1.85 t/MWh and 1.47 t/MWh, respectively. These numbers are taken from Development of Power Generation in South East Europe - Implications for Investments in Environmental Protection Report (World Bank and SEEC). Amount of total CO2 emissions is calculated based on these factors.
Kosovo C CO2 emissions are based on the assumptions that it is employing supercritical technology with 0.84 t/MWh CO2 emission factor.

## Slide 9: Mitigation measures (1)
The World Bank is currently exploring options for channeling this project through CDM mechanisms, possibly combining it with closure of Kosovo A.
Carbon Capture and Sequestration (CCS) technology is being considered as well.
While the power plant may not employ CCS technology in its early phase operation, it is expected that the plant will be CCS ready
  “CCS ready” = Once CCS technology becomes commercially available, and necessary regulatory and economic drivers are in place, it should be capable for rapid retrofit*
Notes: * There is still no standardized definition in regards to the proper meaning of ‘CCS Ready’, but this is considered to be the one that is understood in most cases.

## Slide 10: Mitigation measures (2)
In its efforts to minimize GHG emissions, World Bank is exploring offering the following guidance to Transaction Advisor for incorporation into RFP:
  Specification of technology type; or
  Specification of minimum thermal efficiency; or
  Specification of carbon shadow value or “tax” that would be applied in the bid level of emissions and factored into the evaluation of the bid.